## Slide 1: High-Level Design of a Distribution Microgrid
Senior Design Team 11
Website: https://sddec18-11.sd.ece.iastate.edu/
Client: Alliant Energy
Darin Lamos and Logan Heinen of the Distribution Engineering Department
Faculty Advisor: Professor James McCalley

## Slide 2: Team 11: High-Level Design of a Distribution Microgrid Project Plan - Problem Statement
Alliant Energy has tasked our team with creating a spreadsheet that will calculate the amount of distributed energy needed to meet the kWh demands of a small town in Iowa. This town is miles from the grid and requires long transmission lines to provide power to the town, so it might be more cost effective to create a microgrid in Nichols.
Population: 374
Peak Demand: 630 kVA for 3 hours
Total Annual Load: 2,231 MVA
Fed via grid interconnection

## Slide 3: Project Plan - Conceptual Sketch Team 11: High-Level Design of a Distribution Microgrid

## Slide 4: Project Plan - Functional Requirements Team 11: High-Level Design of a Distribution Microgrid
The simulation of the electric system shall include solar radiation, generation, and load
The solar panel generation and batteries must provide power with minimal load interruption (5% of peak demand)
The spreadsheet will identify the ideal quantity of solar panels and batteries required to meet a user defined portion of the load (80%, 90%, 100%)
The spreadsheet will include hourly demand calculations

## Slide 5: Project Plan - Non-Functional Requirements Team 11: High-Level Design of a Distribution Microgrid
Spreadsheet type deliverable
Visual representations of load demand, generation, and battery supply
Simulation able to run for at least a year of data
Show all calculations and work in a separate tab
Condense all important information together

## Slide 6: Project Plan - Technical Constraints/Considerations Team 11: High-Level Design of a Distribution Microgrid
The final deliverable shall be in the form of an excel spreadsheet
The only sources of power for the microgrid shall be solar panels and batteries
  Supplemental generators are available for demand not met

## Slide 7: Project Plan - Market Survey Team 11: High-Level Design of a Distribution Microgrid
Few island microgrids
Evolving Photovoltaic technology
Remote towns require long transmission lines
Figure 1

## Slide 8: Project Plan - Potential Risks & Mitigation Team 11: High-Level Design of a Distribution Microgrid
Accuracy of future load growth and PV and battery quantities to supply the load
  The growth of a town can only be estimated based on past trends and would affect the growth of the microgrid
  The ratio between the quantity of PV and batteries is dependant on the weather of the microgrid location.
    For example, a location with less solar radiation will require more batteries to supply the load than a location with more solar radiation.

## Slide 9: Project Plan - Resource/Cost Estimate Team 11: High-Level Design of a Distribution Microgrid
Our project does not require any funds
All necessary resources on data and technology specifications for the Nichols system is provided by Alliant

## Slide 10: Project Plan - Project Milestones Team 11: High-Level Design of a Distribution Microgrid
Initial combination of solar and battery capable of supplying enough power
Simulating the microgrid for one week, one month, one year
Implementing supplemental generation and 100%, 90%, and 80% solar supply
Future changes to system to keep up with increasing kWh demand
Use the simulation to model the environment of Nichols, Iowa and prove that the design is capable of supplying enough power to the load.
Applying cost and life cycle analysis to the designed system

## Slide 11: Project Plan - Schedule Team 11: High-Level Design of a Distribution Microgrid
Jan - Mar: Implementation of solar + battery supply of demand
Feb - Mar: Simulation model of environment and output
April: Begin developing Matlab simulation
April: User defined portion of demand supplied by solar panels
April: Finalize simulation and microgrid design, Project Plans, Design Documents, website

## Slide 12: System Design - Functional Decomposition Team 11: High-Level Design of a Distribution Microgrid
Enter input information for the simulation
  Initial battery storage, month of the year, average daily kWh demand, quantity of panels, quantity of batteries
Generate Random Usage
  This simulates the kWh demand for each day of a 1 month period
Generate Random Solar Days
  This simulates the solar radiation for each day of a 1 month period
Print Daily Totals
  This outputs all of the input and output information into tables and visuals for analysis

## Slide 13: System Design - Detailed Design Team 11: High-Level Design of a Distribution Microgrid

## Slide 14: System Design - Detailed Design - Daily Team 11: High-Level Design of a Distribution Microgrid

## Slide 15: System Design - Detailed Design - Monthly Team 11: High-Level Design of a Distribution Microgrid

## Slide 16: System Design - Detailed Design - Yearly Team 11: High-Level Design of a Distribution Microgrid

## Slide 17: System Design - Technology Team 11: High-Level Design of a Distribution Microgrid
Excel VBA Macro Buttons
  Generate random usage profile for the selected month: between 90% and 110% of average daily usage
  Generate random solar profile for the selected month: mixture of low, medium, and high solar days
  Print daily totals for selected month: compiles monthly data in a seperate tab for data analysis
  Combination of these Macros easily allows the user to simulate a full year under various conditions

## Slide 18: System Design - Test Plan Team 11: High-Level Design of a Distribution Microgrid
Achieve Demand
Financial Target
Variable Solar Capabilities
Growth Simulation

## Slide 19: System Design - Implementing Prototype - Nichols, Iowa Team 11: High-Level Design of a Distribution Microgrid

## Slide 20: Conclusion - Current Project Status Team 11: High-Level Design of a Distribution Microgrid
Prototype is capable of..
  Simulating environment including solar radiation and hourly kWh demand
  Supplying user defined portion of load via solar panels and batteries
  Conveying important information such as supplied demand and power generation visually

## Slide 21: Conclusion - Individual Contributions Team 11: High-Level Design of a Distribution Microgrid
Nick - weekly status reports, team website, project planning, test plan, design document
Joe - prototype simulation, load data, user defined supply of kWh demand
Taylor - Solar radiation and generation research, solar + battery implementation for power supply
Minoru - User interface for prototype, solar radiation and generation research, load data
Remo - Matlab simulation, load data organization, financial cost estimates

## Slide 22: Conclusion - Plan for Fall Semester Team 11: High-Level Design of a Distribution Microgrid
Aug: Apply summer data from Nichols to Spring design
Aug: Update Spring prototype
Aug - Sep: Finalize Matlab simulation tool
Sep- Nov: Design system to accommodate for demand growth
Nov - Dec: Apply microgrid design to locations across the US
Nov - Dec: Finalize Senior Design project/ quantity and financial estimations

## Slide 23: Conclusion – Questions? Team 11: High-Level Design of a Distribution Microgrid

## Slide 24: Sources
Figure 1: Metelitsa, Colleen. “U.S. Microgrids 2017: Market Drivers, Analysis and Forecast.” U.S. Microgrids 2017: Market Drivers, Analysis and Forecast | Greentech Media, Nov. 2017
Team 11: High-Level Design of a Distribution Microgrid